### Come from www.eobd2.fr –Voiture française outil de diagnostic Ltd.

### OP-Com 2010 V Can OBD2 Opel:

### http://www.eobd2.fr/opcom-op-com-2010-v-can-obd2-opel-834.html

### Opcom Diagnostics

SECTION 1 : Identification

After selecting "Dignostics", appears a list of years to select the model year (not the year of manufacture). 
For example, my voiturte was manufactured in 2005, while it is a 2006 model. 
To be sure, just double click "Automatic Vehicle Identification"

Then clicking "CAN" windows appear and disappear, leaving the previous window with the vehicle information:

The model now identified, simply go back (Back) and then select the appropriate line. 
Then you select the vehicle:

PART 2 : Diagnostic / Parameterization 
Then comes the different possibilities of diagnosable areas:

Vehicle  -> To identify the vehicle, the items in the car, the numbers of defects per item 
Engine  -> To diagnose the engine 
Transmission  -> To diagnose gearbox, easytronic or automatic 
Chassis  -> ABS / TC / ESP, Pressure Sensors, Power Steering, Active Suspension 
Body  -> Open & Start, Dashboard, Removable roof, Airbag, Central Air Conditioner, AFL, Park Pilot, front fuse box (UEC) and rear (REC) 
Infotainment System  -> Car, screen, Optional phone DAB

VEHICLE:

- For Identification  -> Returns to what has been seen previously to identify the vehicle

- Module / ECU Presence Check  -> To detect elements present in the car and check that they communicate well

- Vehicle DTC Information  -> The same thing but with the number of DTC by this element. 
By double clicking on a line leads directly to the element.

We can see for example in my case, the unit is no longer communicating because I changed a GTCE8919

ENGINE:

We must select the engine for your car, present on the login page seen above:

The OPCOM connects to the engine and displays its characteristics, including the software release:

- Fault Codes  displays fault codes related here to the engine.

- Measuring Blocks  allow to display the values ​​of the various parameters, sensors, voltages:

The first button  displays the values ​​of various engine parameters ...

Engine Oil Status  Used to determine the degradation of the oil. We can see that mine is to change !!

Read Odometer Value displayed just the mileage of the vehicle:

- Output Tests allow to execute tests on the engine components. Be careful not to do anything !!

Programming allows you to program some motor parameters as the circumference of the wheels, or just the vehicle identification number.  Be careful not to do anything !!

This identification number must be the same for all the car element !! This number must be entered every time you install a new item as a new original radio or when you change the screen. 
Beware the ECU reset function, it resets the engine control unit. After, it does not work and requires Adobe Tech2 to be reconfigured. It is the same for all the other computers.

This architecture is valid for all searchable items with OPCOM.